## Slide 1: RETIMING and UNFOLDING
Dr.Elwin Chandra Monie
Dept. of ECE, RMK Engineering College

## Slide 2: Transformations
Retiming and unfolding used to bring out and exploit hidden concurrency in the algorithm
Use these transformation to increase the efficiency in implementation
Refer:
Keshab K. Parhi, ‘Algorithm transformation techniques for concurrent processors’, Proc. IEEE, Dec.,1989, pp. 1879-1895

## Slide 3: Retiming
Moving around delays without affecting the input/output characteristics of the system
Can reduce the critical path of the system
Does not alter the latency of the system
Minimize
  Clock period
  No. of registers

## Slide 4: Nodal Transfer
2D
r(a) = number of delays transformed from outgoing edges
to incoming edges of node a
4D
v
u
3D
D
D
D
Edge e
v
u
2D
r(v) = - 1 r(u) = 1
Notes: We illustrate the process of transfer of delays through a node without changing functionality (See [Madisetti95] for further details).

## Slide 5: Reduction of clock period
After retiming the clock period is reduced to 2 units (33% reduction)
Placing register at the input of the nodes can reduce switching activities that leads to reduced dynamic power
Critical Path =3
Critical Path =2
1
2
3
4

## Slide 6: Retiming Solution
Weight of edge from node U to node V in the retimed graph is
wr (e) = w(e) + r(V)-r(U)
where r( ) is the lag parameter
e.g r(1)= 0; r(2)=1; r(3)=0; r(4)=0
wr (3→2) = w(3→2) + r(2)-r(3) = 0+1-0=1
Retiming is feasible if wr (e) ≥ 0 for all edges

## Slide 7: Properties of Retiming
1. The weight of the retimed path
p = V0 →V1 →V2 …… → Vk is given by wr(p) = w(p) + r(Vk) - r(V0)
2. Retiming does not change the number of delays in a cycle
3. Retiming does not alter the iteration bound
4. Adding a constant value to the retiming value of each node does not change the mapping from G to Gr

## Slide 8: Proof 1
p =V0 →V1 →V2 …… → Vk

## Slide 9: Proof 2
If Vk = V0
wr(c)=w(c)
Then retiming does not change the no.s delays in a cycle

## Slide 10: Proof 4
wr (e) = w(e) + r(V)-r(U)
Add j to node V and node U
wr (e) = w(e) +( r(V)+j)-(r(U)+j)
wr (e) = w(e) + r(V)-r(U)
There is no change

## Slide 11: Unfolding
Unfolding is the method of processing individual iterations of the loop separately

## Slide 12: Algorithm for Unfolding
For each node U in the original DFG, draw J node U0 , U1 , … UJ-1
For each edge U → V with w delays in the original DFG, draw the J edges
Ui → V(i+w)%J with
delays for i=0,1,2… J-1
In J unfolded DFG for w<J Unfolding of an edge with w delays in the original DFG produces J-w edges with no delays and w edges with 1 delay
J- Unfolding
J = 4
w >J

## Slide 13: Properties of Unfolding
Unfolding preserves precedence constraints
Unfolding preserves the number of delays in a DFG
J-unfolding of a loop l with wl delays in the original DFG leads to gcd(wl ,J) loops in the unfolded DFG and each of these loops contains wl / gcd(wl ,J) delays and J/gcd(wl ,J) copies
of each node that appears in l
J-unfolding a DFG with iteration bound
T∞ results in a iteration bound JT∞

## Slide 14: Sample Period reduction
Iterative Bound T∞ is the lower bound on the iteration or sample period
But in many cases sample period cannot be equal to Iterative bound without any transformation
Cases where sample period is equal to iterative period is not possible normally
  Case 1: A node in the DFG having computation
  time more than iterative period
  Case 2: Iterative bound is not an integer

## Slide 15: Sample Period reduction …..
Unfolding allows DFG with iteration period (sample period) equal to iteration bound to be implemented
Case 1
A node in the DFG having computation time more than iterative period
Iterative bound is 3ut
Since S and T have 4ut minimum sample period possible is 4ut

## Slide 16: Sample Period reduction …..
2-Unfolded has iteration bound of 6ut
This unfolded DFG perform 2 iterations of the original
So the sampling period is 6/2 = 3ut, same as T∞
If the computation time of the node U, tu is greater than T∞ then tu/T∞ unfolding should be used
tu=4 ; T∞ =3
So 4/3 unfolding or 2-unfolding is used
D
D
D
2D
2-Unfolding

## Slide 17: Sample Period reduction …..
Case 2
  Iteration bound is not an integer
If the critical loop bound is of the form t1/w1 where t1 and w1 are co-prime then w1-unfolding should be used
e .g. t1=60 and w1=45 then t1/w1 =4/3 and 3-unfolding should be used

## Slide 18: Parallel Processing
Word level Parallel Processing
Bit level Parallel Processing
  Bit Serial processing
  Bit parallel processing
  Digit parallel processing

## Slide 19: Parallel Processing …
Word serial ⇒ Word parallel
3-unfolded

## Slide 20: Unfolding a node with a switch
Unfolding an edge with a switch from node U to node V
Assume
  W=W’J and edge has no delays
In the unfolded graph draw from the node Uu%J to Vu%J which is switched at instance (W’l+⎿u/J⏌)

## Slide 21: Unfolding a node with a switch …
u=1 U1 ⇒ V1
At 4l+0 instance
u=7 U1 ⇒ V1
At 4l+2 instance
u = 9 U0 ⇒ V0
At 4l+3 instance
u=11 U2 ⇒ V2
At 4l+3 instance

## Slide 22: Bit-Serial to Bit-Parallel Adder
Z0
XX
D0
A0
B0
S0
D0
A1
B1
S1
D1
Z1
X0
X1
2l+0
2l+1
D
D
2l+0
0
a2 b2
a0 b0
a3 b3
a1 b1
s2 s3
s0 s1
2l+1
+
+
Digit-serial Adder
2-unfolded