## Slide 1: HW/SW CODESIGN OF THE MPEG-2 VIDEO DECODER
Matjaz Verderber, Andrej Zemva, Andrej Trost
University of Ljubljana
Faculty of Electrical Engineering
Trzaska 25, 1000 Ljubljana, Slovenia
matjaz.verderber@fe.uni-lj.si

## Slide 2: Hw/Sw Partitioning – Single-Spec Assumption
Assumption – Start from a single specification
  Typically sw source
Partitioning
  Find critical sw kernels, map some to hw
This assumption is made in most research efforts as well as commercial tools
Hw/sw partitioner
Sw
Hw
Specification
Compilation
Synthesis
Binaries
Netlists

## Slide 3: Presentation outline
Motivation and basic idea
Optimization of the MPEG-2 video decoder
  Timing optimization
  Power consumption analysis
FPGA implementation of the MPEG-2 video decoder
  System environment
  Implementation in the FPGA
  Implementation results
Conclusion
Motivation and basic idea

## Slide 4: Motivation and basic idea
Importance of the MPEG-2 standard
Real-time requirements and low-power operation
Possibilities to use modern HW/SW technology
HW/SW optimization and implementation within one FPGA
  Software tool for MPEG simulations
  Analysis (time, power consumption) of the MPEG-2 decoder
  Optimization (time, power consumption)
  Implementation in Virtex 1600E
Timing optimization

## Slide 5: Timing optimization
ISO/IEC 13818-2 compliant software MPEG-2 decoder
Diagram of the Lei-Sun VLC decoder
Hardware implementation
Modified Chen 1D inverse DCT
Hardware implementation
Timing optimization

## Slide 6: Timing optimization
Up to 40% improvement of speed for MPEG-2 decoding compared to software based solution
Decoding times for 150 sequences before and after optimization
72 MHz - estimated decoding frequency for real-time decoding (after optimization)
Power consumption optimization

## Slide 7: Power consumption optimization
Conclusions have been made based on energy conscious study made by Henkel and Li
Correlated results by timing and power consumption optimization
Results of the case study
Case 1 - Quant. in HW, the rest in SW
Case 2 - 2-D DCT in HW, the rest in SW
Case 3 - 1-D DCT in HW, the rest in SW
Case 4 - Quant. and 2-D DCT in HW,
the rest in SW
System environment

## Slide 8: System environment
HW/SW partitioned MPEG-2 decoder has been tested on the Flextronics FPGA based prototyping board
4 Mbyte SRAM
Xilinx Virtex 1600E (2188742 system
gates, 72x108 CLBs, 589824 bits of
RAM, ...)
64 Mbyte SDRAM
32 Mbyte Flash
Several peripheral HW cores (RISC, VGA, UART, MEMC) described in Verilog
Implementation in the FPGA
Different Linux-uClinux software tools available (GCC, GDB, Simulator, …)

## Slide 9: Implementation in the FPGA
Block diagram of the implemented MPEG-2 decoder
Hardware implementation
Software implementation
Error messages and warnings
Boot up sequence
Working memory
Access to external devices
Stored MPEG-2 decoder software
Display of the decoded frames
WISHBONE BUS
Implementation results

## Slide 10: Implementation results
40% utilization of the Virtex 1600E
Implementation results of the MPEG-2 decoder
Synplify Pro (synthesis) and Xilinx ISE Foundation software (implementation) used
All cores described in Verilog
Conclusion

## Slide 11: Conclusion
Optimized MPEG-2 video decoder by speed and power consumption
40% higher decoding speed and 36% lower power consumption
Some problems by final routing
Presentation of a modern implementation method where complex embedded system (MPEG-2 decoder) can be efficiently HW/SW partitioned