## Slide 1: Synchronous, Wave and Asynchronous pipeling
Elwin Chandra Monie, R M K Engineering College

## Slide 2: Clock period in a Pipeline
Consider a s-stage pipeline with stage delay tstage
One set of inputs is applied to the pipeline at time t1
At time t1 + tstage + t, partial results are safely stored in latches
Apply the next set of inputs at time t2 satisfying t2  t1 + tstage + t
Therefore:
Clock period = t = t2 – t1  tstage + t
Throughput = 1/ Clock period  1/(tstage + t)

## Slide 3: Clock skew
Two implicit assumptions in deriving the throughput equation below:
One clock signal is distributed to all circuit elements
All latches are clocked at precisely the same time
Throughput = 1/ Clock period
 1/(tstage + t)
Uncontrolled or random clock skew
causes the clock signal to arrive at
point B before/after its arrival at point A
With proper design, we can place a bound ±e on the
uncontrolled clock skew at the input and output latches of a
pipeline stage
Then, the clock period is lower bounded as:
Clock period = t = t2 – t1  tstage + t + 2e

## Slide 4: Wave Pipelining
The stage delay tstage is really not a constant but varies from tmin to tmax
tmin represents fast paths (with fewer or faster gates)
tmax represents slow paths
Suppose that one set of inputs is applied at time t1
At time t1 + tmax + t, the results are safely stored in latches
If that the next inputs are applied at time t2, we must have:
t2 + tmin  t1 + tmax + t
This places a lower bound on the clock period:
Clock period = t = t2 – t1  tmax – tmin + t
Thus, we can approach the maximum possible pipeline throughput of 1/t without necessarily requiring very small stage delay
Two roads to higher pipeline throughput:
Reducing tmax
Increasing tmin

## Slide 5: Ordinary Vs Wave pipeling
(a) Ordinary pipelining
(b) Wave pipelining

## Slide 6: Random Clock Skew in Wave Pipelining
Clock period = t = t2 – t1
 tmax – tmin + t + 4e
Reasons for the term 4e:
Clocking of the first input set may
lag by e, while that of the second
set leads by e (net difference = 2e)
The reverse condition may exist at
the output side
Uncontrolled skew has a larger
effect on wave pipelining than on
standard pipelining, especially
when viewed in relative terms